| MDR774M 2.4GHz BPF for Wireless LAN |  |
| --- | --- |

Characteristics

MDR774M Zin/Zout 50 ohm Nominal Fc 2450MHz Nominal Pass Band 2400-2500MHz Insertion Loss 1.5 dB max (2400-2500MHz at 25 Deg.C) 1.7 dB max (2400-2500MHz at -40 up to +85 Deg.C) Ripple 0.6 dB max (2400-2500MHz at 25 Deg.C) V.S.W.R 2.0 max Attenuation 30 dB min (880-915MHz) 30 dB min (1710-1785MHz) 25 dB min (1850-1910MHz) 30 dB min (4800-5000MHz)

Number of ordered pieces

2000pcs/Reel

Dimensions

Frequency Data1

Frequency Data2

Land Pattern

Resist Pattern

Taping Dimensions

Reel Dimensions